## Slide 1: Tariq Yousuf (804805977) & Mark Geha (704769079)
Design Features
Significant Pipelining, Parallelism and Scheduling allowing for a design with only 20 multipliers total
Technology | Synopsys 32nm
Total Area | 689809.98
Total Power | 768 mW
Energy/Image | 1.23 uJ/Image
Delay | 800 clock cycles (1600 ns)

## Slide 2: High-Level Design Optimizations
Implementing 10 separate Neurons so that multiplications and additions can occur in parallel
Scheduling the weight-pixel multiplications so that only two sets of weight-pixels are processed consecutively for each Neuron
Aggressive pipelining in the multipliers and adders in order to allow for an 800-clock cycle latency with minimal hardware
Final design only needs 20 multipliers and 30 adders in an effort to reach minimal area

## Slide 3: Further Optimizations
Refactoring of components when possible to reduce hardware and interconnects
Addition of an accumulator for each Neuron to reduce necessary flip-flops needed to store intermediate results
Computing the bias weights using left-shifters rather than multipliers
No Sigmoid function implemented while maintaining 86% accuracy to reduce hardware